## Slide 1: TPMS870000-SKT 29152 revB Hardware setup
For TPMS FXTH/MKW01 LF RF Communication Reference projects
January 2017

## Slide 3
3.3V power supply
Not connected

## Slide 4
Please note:
The RF matching network of this board has not been optimized so the RF performance achieved is not the best one possible. Due to that, all the RF configurations (antenna grounded or not, use of clip antenna or external antenna connected to SMA) give the same RF performance. So on this board the default configuration can be kept (use of clip antenna not grounded), there will be no improvement with another configuration.
Refer to slide 6 for additional information on RF setup.

## Slide 6: About RF setup
The matching network on the FXTH SKT board is not optimized so make sure you are in good conditions when using the board: distance emitter/receiver around 35cm with no obstacle in-between.
If the RF performance is not good i.e. there is a high rate of data loss or data corruption (CRC check fails – this can be seen in the GUI), then try to change the distance and/or the orientation between the FXTH and the MKW01:
  Decrease or increase the distance, even by a few cm: change the distance and check the result real-time by looking at the MKW01 CRC window in the GUI.
  Change the orientation of the FXTH socket: place it parallel or perpendicular to the KW01 board, rotate it by 90°, 180°, and check the result real-time by looking at the MKW01 CRC window in the GUI.
Example: a few cm can make a significant difference on the data corruption rate
Distance FXTH/MKW01 of 30cm
Distance FXTH/MKW01 of 35cm
Note: in order to display the frames with corrupted data (when CRC is 1 in the GUI), make sure that RF_DATA_CORRUPTED is defined as RECEIVE_DATA in the MKW01 project (RF_Rx_Apli.h).

## Slide 7: Connecting the P&E micro multilink
3.3V power supply
Connected to the computer
Both LEDs must be ON