## Slide 1: FRDM-SENSORS-LF MRB-KW019032 or FRDM-KW019032 Hardware setup
For TPMS FXTH/MKW01 LF RF Communication Reference projects
January 2017

## Slide 2
FRDM-SENSORS-LF 29153 revB
+ MRB-KW019032 rev C or D
LED16 (PTC2)
ON while an RF frame is received and displayed
LED10 (PTE1)
ON while an LF frame is sent
LED15 (PTE16)
ON during 200ms when an unknown command is received from the Sensor GUI
LED4 (PTA4) and LED5 (PTE0)
They can be turned ON and OFF with commands from the Sensor GUI
Note: both MRB-KW019032 revC and D can be used for the demo (jumpers and connections are the same).
The only difference between the two revisions is that UART RTS/CTS flow control can be implemented with revD (and not with revC), but this is not used in the demo.

## Slide 3: MRB-KW019032 rev C
J3
DIO4 connected to PTD4 (this is not used in the demo project so it can be disconnected if needed)
RF antenna
J8 [1->2]
DIO5/CLKOUT connected to PTA18 for clock source. Do not disconnect.
J7
PTE30 connected to radio reset.
Used in the project, do not disconnect.

## Slide 4: MRB-KW019032 rev D
J3
DIO4 connected to PTD4 (this is not used in the demo project so it can be disconnected if needed)
J17 (different from rev C)
Access to PTB2 and PTB17 (instead of UART RTS/CTS). They are not currently used in the project so jumper configuration can be modified if needed.
RF antenna
J8 [1->2]
DIO5/CLKOUT connected to PTA18 for clock source. Do not disconnect.
J7
PTE30 connected to radio reset.
Used in the project, do not disconnect.

## Slide 5: MRB-KW019032 rev C or D P&E Multilink connection
Connected to the computer to supply the board
Multilink connected to the computer
Both LEDs must be ON

## Slide 6
J140
Power supply, do not disconnect.
Spare jumpers, they are not connected
Spare jumpers, they are not connected
Connected jumpers
LF antenna power supply.
2 possibilities:
Connect the external power supply with wires as shown in the photo;
Place a battery in the battery holder on the other side of the board.
The antenna can be supplied between 5V and 18V maximum.
Typical power supply: 9V for a distance emitter/receiver of 35cm free air.
If the LF signal is received but the data not decoded (result is unknown command), the LF coil is probably saturating (signal too strong). In this case try to increase the emitter/receiver distance.
If the LF signal is not strong enough (not received by the FXTH), increase the power supply.
FRDM-SENSORS-LF
29153 revB

## Slide 7
Connected jumpers

## Slide 9: FRDM-SENSORS-LF 29153 revB + FRDM-KW019032 revA
Please note: when using the FRDM-KW019032 revA, some LEDs on the FRDM-SENSORS-LF will not be turned ON with full luminosity (like LED5, LED10, LED16). This is due to the level shifters on the FRDM boards that cannot provide enough current.
If needed, change the LED configuration in the KW01 project to select LEDs connected to GPIOs that do not go through level shifters on the FRDM board.

## Slide 11: Modifications to operate in order to use the FRDM-KW019032 revA connected to the FRDM-SENSORS-LF for the TPMS reference projects
 | FRDM-KW019032 Rev A | 
PTB0 | LF PREMO OUT2 | Populate R132
PTA19 | LED3 VTRIG4 | Populate R136
PTA19 to DIO4 |  | Trace J10 cut
PTA4 | LED4 | Populate R133
To source J3.6 and IO_REF: populate R138 (3.3V) |  | Populate R138
To source 3.3V to J3.10: populate R127 |  | Populate R127
PTD6 | RST_GPIO | Populate R134
PTE17 | ADC2 | Populate R135
To source 5V to J3.12: populate R140 |  | Populate R140
PTE16 | LED15 | Populate R137
PTB17 | LED7 & VTRIG1 | DNP R90 PTB17 CTS
PTB2 | LED6 & VTRIG2 | DNP R91 PTB2 RTS
 |  | Remove if FTDI only: R89: PTA1/UART0_RX <=> UART1_RX_TGTMCU
 |  | Remove if FTDI only: R88: PTA2/UART0_TX <=> UART1_TX_TGTMCU
PTE0 | LED5 | J44 to be populated
PTE1 | INT for 3115 | J43 to be populated

## Slide 12: FRDM-KW019032 revA
[2 -> 3]
[1 -> 2]
Be careful: some hardware modifications (other than jumpers) need to be performed on the board in order to use it connected on the FRDM-SENSORS-LF board for the TPMS reference projects.
Refer to previous slide.

## Slide 14: FRDM-KW019032 P&E Multilink connection

## Slide 15: About RF setup
The matching network on the FXTH SKT board is not optimized so make sure you are in good conditions when using the board: distance emitter/receiver around 35cm with no obstacle in-between.
If the RF performance is not good i.e. there is a high rate of data loss or data corruption (CRC check fails – this can be seen in the GUI), then try to change the distance and/or the orientation between the FXTH and the MKW01:
  Decrease or increase the distance, even by a few cm: change the distance and check the result real-time by looking at the MKW01 CRC window in the GUI.
  Change the orientation of the FXTH socket: place it parallel or perpendicular to the KW01 board, rotate it by 90°, 180°, and check the result real-time by looking at the MKW01 CRC window in the GUI.
Example: a few cm can make a significant difference on the data corruption rate
Distance FXTH/MKW01 of 30cm
Distance FXTH/MKW01 of 35cm
Note: in order to display the frames with corrupted data (when CRC check is 1 in the GUI), make sure that RF_DATA_CORRUPTED is defined as RECEIVE_DATA in the MKW01 project (RF_Rx_Apli.h).