## Slide 1: Session 2
Mats Pettersson, Sr FAE IAR Systems US
Notes: <number>

## Slide 2
EWARM and MQX
MQX and its different components
The MQX library structure
EWARM Workspace for MQX
MQX build and project options in EWARM

## Slide 3
About Freescale MQX
The Freescale MQX Real-Time Operating System (RTOS) provides real-time performance within a small, configurable footprint.
MQX is a run-time library of functions that programs use to become real-time multi-tasking applications. The main features are its scalable size, component-oriented architecture, and ease of use.
MQX supports multi-processor applications and can be used with flexible embedded I/O products for networking, data communications, and file management.

## Slide 4
MQX libraries
SMQX contains of, among other things, a set of libraries with their own API.
BSP, Board Support Package
PSP, Processor Support Package
RTCS, TCP/IP stack (Communication Suite).
MFS, Embedded File System
SHELL, Shell for RTCS
USB_DDK, USB device
USB_HDK, USB host

## Slide 5
MQX installation structure
mfs, mqx, rtcs, shell and usb: These folders contains the - source code for the different modules - example code - projects to build the module and examples
doc: Contains - documentation for the API’s - Reference manuals - Getting started guides

## Slide 6
MQX installation structure
config: Workspace and configuration files to build your MQX libraries
lib: Location where built libraries and header files are copied to
tools: Various tools that can be useful, for example tools to convert HTML file to C arrays.

## Slide 7
Library folders
”config\<board>”
EWARM Workspace file (*.eww)
user_config.h
”lib\<board>.iar”
Built libraries
Copied header files
Libraries are built with or without debug information Without information: <lib>_<board>.a
With debug information: <lib>_<board>_d.a

## Slide 8
user_config.h
Compile-time configuration of all key Freescale MQX RTOS components (PSP, BSP, RTCS, MFS, USB, ...) is accomplished by editing the user_config.h file.
Note that user_config.h includes other *_config.h files.
We will only modify the channel used for stdio. By default UART is used, and we will change that to use the debugger communication channel.

## Slide 9
user_config.h
Modifying user_config.h requires that the used MQX libraries are rebuilt!
See MQX User Guide for fine tuning…
3.14 Configuring MQX at Compile Time
3.14.1 MQX Compile-Time Configuration Options
3.14.2 Recommended Settings

## Slide 10
Modifying the stdio communication channel
For MQX applications two configuration files needs to be modifed.
user_config.h
twrk60n512.h
In user_config.h
#define BSPCFG_ENABLE_IODEBUG 1
In twrk60n512.h #define BSP_DEFAULT_IO_CHANNEL "iodebug:“ #define BSP_DEFAULT_IO_CHANNEL_DEFINED

## Slide 11
Building MQX libraries
Manually build each library
Using ”Batch build” to build a set of predefined libraries
All EWARM MQX library projects have a set of predefined batch builds
All, that will build all MQX libraries for debug and release
Debug, that will build all MQX debug libraries
Release, that will build all MQX release libraries

## Slide 12
Building MQX libraries
The generated library and header files are copied to “lib\<board>.iar”.
This is done with the post-build command in EWARM.

## Slide 13
Building MQX libraries
Here we have the EWARM projects located and this is the location where the different MQX modules will be built.
Once a module is built, then that library and header files will be copied to the “lib”.
Here is where the EWARM MQX library Workspace is located together with the different build time configuration files.

## Slide 14
Batch builds
You can create any number of your own batch builds.
Project menu -> Batch build…
New
Add a name
Select config
Order build
Click “OK”

## Slide 15
Hands-on session 2