## Slide 1: Session 3
Mats Pettersson, Sr FAE IAR Systems US
Notes: <number>

## Slide 2
Creating our own MQX based application
Create a new EWARM project
Add MQX libraries
Add application code
Setting up project options
Build and debug

## Slide 3
Some considerations
When creating an MQX based project there are many things we need to consider.
We will not worry about most of them, but just the few mentioned below.
Use a EWARM Workspace with only the application, or the application and MQX library?
Using batch builds or not?
What libraries/modules of MQX will I be using?

## Slide 4
What we will do
Create a Workspace with just our own MQX based application
Add libraries and create our MQX application code
Set up our project options
Build and debug our application
Add the BSP and PSP library projects to our Workspace
Create one Debug and one Release Batch build for our system

## Slide 5
Our MQX application
Our example application will be very similar to the Hello2 example application included in MQX.
We will however create our own project from scratch in order to see all the steps needed to create your own MQX based application. At a minimum we will need to define one task and the the array “MQX_template_list”.
Our application will have two task. One that start automatically, and the other is created and started by the first task.

## Slide 6
Linking
So far we have only built libraries for MQX and have not had to consider linking our application.
To make sure that all the parts of MQX and our application is located correctly in memory we use the linker configuration file (*.icf).
Easiest is to use one of the premade ICF files for EWARM and MQX located at; “mqx\source\bsp\twrk60n512\iar”
for example “intflash.icf”.

## Slide 7
MQX memory layout
FLASHX_POOL
ro
TEXTSECTION
CFMPROTROM
.intvec
KERNEL_DATA
USER_DEFAULT_MEMORY
.vector_ram
0x0007 FFFF
0x0000 0000
0x2000 FFF0
0x1FFF 0000
First in RAM
Last in RAM
Always at address 0x00
Last in ROM/Flash

## Slide 8
Hands-on session 3