## Slide 1: Session 4
Mats Pettersson, Sr FAE IAR Systems US
Notes: <number>

## Slide 2
More project managment
Add a second application project to our Workspace
Add new Batch Builds to handle the different application projects
Using pre/post-build to automate the build process
  Get our web pages re-compiled
Extending the Embedded Workbench tool chain
About header include files in EWARM projects

## Slide 3
More Batch Builds to our Workspace
Application 1 - Release
Application 1 - Debug
Application 2 - Release
Application 2 - Debug
BSP – Release
BSP – Debug
PSP – Release
PSP – Debug
RTCS – Release
RTCE - Debug
All
All Debug
App 1 Debug
App 2 Release
BSP – Release
BSP – Debug
PSP – Release
PSP – Debug
RTCS – Release
RTCE - Debug
Application 1 - Release
Application 1 - Debug
Application 2 - Release
Application 2 - Debug
BSP – Debug
PSP – Debug
RTCE - Debug
Application 1 - Debug
Application 2 - Debug
BSP – Debug
PSP – Debug
RTCE - Debug
Application 1 - Debug
BSP – Release
PSP – Release
RTCS – Release
Application 2 - Release
Project – Configuration Batch Build Project-Configuration build order

## Slide 4
Build actions
You can add both pre- and post-build actions to a project
For MQX libraries we already use post-build to copy files to a specific loaction.
For our web server application we will create a pre-build action that will convert web pages to C arrays that we include when building our project. For this we will make a modified version of the mktfs.bat bat file that comes with MQX.
mktfs.bat calles the MQX tool mktfs.exe to convert web pages into C arrys in the file tfs_data.c.

## Slide 5
Using pre-build
REM *** mktfsEW.bat ***
cd %1\..
..\..\..\tools\mktfs.exe web_pages
"$PROJ_DIR$\..\mktfsEW.bat" "$PROJ_DIR$"
This is our bat file that we call from the IDE’s pre-build
This is the command line we use in pre-build
$PROJ_DIR$ - an EWARM IDE variable that expands to the location of the current project file.
$TOOLKIT_DIR$ - Embedded Workbench installation directory
$EXE_DIR$ - the directory for executable output
Many more available!. See the EWARM IDE guide, section “Argument variables”.

## Slide 6
Extending the toolchain
IAR Embedded Workbench provides a feature—Custom Build—which lets you extend the standard toolchain.
This feature is used for executing external tools and you can make these tools execute each time specific files in your project have changed.
This option is, if used, specified for each project and is setup in: Project options -> Custom Build.
We could use this tool to create C arrays from HTML files. If we did, then we could just add a HTML file to our project tree and this custom build tool would generate the C array just before the C files are compiled!

## Slide 7
About the Workspace project tree
Header files added to the project tree are not included in the build!
The compiler and assembler will only search the standard include directories, plus the additional directories specified in the their “Preprocessor” option.
This cm.h might, or might not, be used during the build.
To find the cm.h used, expand cm.c.

## Slide 8
About MQX projects and user_config.h
Be careful if you add header file to your project.
In most cases this is not a good idea!
For MQX libraries, adding user_config.h is a great idea!
This is because user_config.h is being copied to new locations and it is easy to modify the wrong user_config.h.

## Slide 9
Hands-on session 4