## Slide 1: NXP Power Solution for Xilinx FPGA
Aug.2026
APS AE Team

## Slide 2: Xilinx Artix™ 7 Power Solution
NXP PMIC | Rails used | Key features
PF8150 | 7 buck converters + 4 LDO/load switches | Single-chip supply for the Artix™-7 FPGA and DDR4 memory; high-current multi-rail design saves board space; OTP-configurable rails.
Note: The power solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
PF8150 PMIC
Xilinx Artix™ 7 - FPGA
BUCK1
BUCK2
BUCK3
BUCK4
BUCK5
BUCK6
BUCK7
LDO1/LS
LDO2/LS
LDO3/LS
LDO4/LS
VCCINT
VCCBRAM
VMGTRAVCC
VMGTRAVTT
VCCO_3V3
VCCO_IO_3V3
VCC_AUX
VCC_ADC
VCCO_2V5
VCC_IO_2V5
DDR4
VDD
VTT
2.7 V– 5.5 V
0.9 V, 0.95 V, 1.0 V @ 5 A
1.0 V @ 5 A
1.2 V @ 2.5 A
3.3 V @ 2.5 A
1.8 V @ 0.4 A
2.5 V @ 0.4 A
0.6 V @ 2.5 A
Reserved
Reserved
NXP Technology
Non-NXP Technology
VIN

## Slide 3: Xilinx Artix™ 7 High Performance Power Solution
NXP PMIC | Rails used | Key features
PF53, PF52, PF7100 | PF53: 1 buck; PF52: 1 buck; PF7100: 5 bucks + 2 LDO/LS | Scalable high-current multi-rail solution for high-performance Artix™-7 and DDR4 designs.
Note: The power solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
PF53
VIN
PF52
VIN
PF7100
VIN
2.7 V – 5.5 V
BUCK1
BUCK1
BUCK1
BUCK1
BUCK2
BUCK3
BUCK4
BUCK5
LDO1/LS
LDO2/LS
Xilinx Artix™ 7
High Performance - FPGA
VCCINT
VCCBRAM
VMGTRAVCC
VMGTRAVTT
VCCDDR
VCCO
VCCO_IO
VCCAUX
VCCADC
VDD
VTT
DDR4
0.95 V, 1.0 V @ 10 A
1.0 V @ 8 A
1.2 V @ 8 A
1.2 V @ 5 A
2.5 V, 3.3 V @ 2.5 A
1.8 V @ 0.4 A
0.6 V @ 5 A
Reserved
NXP Technology
Non-NXP Technology

## Slide 4: Xilinx Spartan™ 7 Power Solution 1
Note: The power solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
NXP PMIC | Rails used | Key features
PF5103 | 3 buck converters + 2 LDOs | Single-chip power solution for Spartan™-7 and DDR3; reduced BOM and design complexity.
PF5103 PMIC
Xilinx Spartan™ 7 - FPGA
VIN
5 V
BUCK1
BUCK2
BUCK3
LDO1
LDO2
VCCINT
VCCO_3V3
VCC_AUX
VCC_2V5
DDR3
Reserved
1.2 V @ 3.5 A
1.35 V @ 3.5 A
3.3 V @ 3.5 A
2.5 V @ 200 mA
NXP Technology
Non-NXP Technology

## Slide 5: Xilinx Spartan™ 7 Power Solution 2
Note: The power solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
NXP PMIC | Rails used | Key features
PF53 + PF5123 | PF53: 1 high-current buck PF5123: 3 bucks | Scalable power solution for Spartan™-7 and DDR3 applications; supports higher-current FPGA designs.
PF53 PMIC
PF5123 PMIC
Xilinx Spartan™ 7 - FPGA
VIN
VIN
5 V
BUCK1
BUCK1
BUCK2
BUCK3
VCCINT
VCCO_3V3
VCC_AUX
VCC_2V5
DDR3
1.2 V @ up to 15 A
1.35 V @ 3.5 A
3.3 V @ 3.5 A
2.5 V @ 3.5 A
NXP Technology
Non-NXP Technology

## Slide 6: Xilinx Kintex UltraScale_AU10P/15P Power Solution
FS56
VSUP
ENx
SW2
SW1
PGOOD
I2C
12 V / 24 V VBAT
Wake up
MCU
POWER
POR
I2C
GPIO
GPIO
3.3 V/5 V@3 A
*Optional for 12 V vehicle battery systems
PF8150
VIN
PWRON
PGOOD
I2C
3.3 V @ 10 A
2.7 V – 5.5 V
Artix US+ (AU10P/15P) - FPGA
VMGTAVTT
VCCINT, VCCBRAM, VCCINT_IO
VCCAUX/ADC
VMGTAVCC
VMGTVCCAUX
VCCO
1.2 V @ 3 A
0.72 V / 0.85 V @ 1.5 A
1.8 V @ 0.35 A
0.9 V @ 0.75 A
1.8 V @ 0.15 A
1.0 V/3.3 V @ 1.5 A
DDR
VDD
VPP
VDDQ/2
VDDQ
1.2 V @ 5 A
DDR
terminator
2.5 V @ 0.4 A
NXP Technology
Non-NXP Technology
NXP PMIC | Rails used | Key features
FS56 + PF8150 | FS56: 2 switchers; PF8150: 7 bucks + 4 LDOs | Integrated power platform for Kintex™ UltraScale+ AU10P/15P, optimized for industrial vision, sensor fusion and automotive applications.
Note: The power solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
Optional Technology
Reserved
5
1
2
3
4
6
BUCK1
0.4 V to 1.8 V @ 2.5 A
BUCK2
0.4 V to 1.8 V @ 2.5 A
BUCK3
0.4 V to 1.8 V @ 2.5 A
LDO3
1.5 V to 5.0 V @ 0.4 A
LDO3
1.5 V to 5.0 V @ 0.4 A
BUCK5
0.4 V to 4.1 V @ 2.5 A
BUCK6
0.4 V to 4.1 V @ 2.5 A
LDO1
1.5 V to 5.0 V @ 0.4 A
BUCK4
0.4 V to 1.8 V @ 2.5 A
LDO2
1.5 V to 5.0 V @ 0.4 A
BUCK7
1.0 V to 4.1 V @ 2.5 A

## Slide 7: Xilinx Kintex UltraScale_AU20P/25P Power Solution
FS56
VSUP
ENx
SW2
SW1
PGOOD
I2C
MCU
POWER
POR
I2C
GPIO
GPIO
*Optional for 12 V vehicle battery systems
PF53
VIN
PWRON
I2C
BUCK1
0.4 V to 1.8V @ 8 A
PF8150
VIN
PWRON
PGOOD
I2C
BUCK1
0.4 V to 1.8 V @ 2.5 A
BUCK2
0.4 V to 1.8 V @ 2.5 A
LDO1
1.5 V to 5.0 V @ 0.4 A
BUCK4
0.4 V to 1.8V @ 2.5 A
LDO2
1.5 V to 5.0 V @ 0.4 A
BUCK7
1.0 V to 4.1 V @ 2.5 A
BUCK5
0.4 V to 4.1 V @ 2.5 A
BUCK6
0.4 V to 4.1 V @ 2.5 A
Artix US+
(AU20P/25P) - FPGA
VMGTAVTT
VCCINT, VCCBRAM, VCCINT_IO
VCCAUX/ADC
VMGTAVCC
VMGTVCCAUX
VCCO
DDR
VDD
VPP
VDDQ/2
VDDQ
3.3 V @ 10 A
2.7 V – 5.5 V
3.3 V/5 V
@ 3 A
0.85 V @ 15 A
1.2 V @ 3 A
1.8 V @ 0.35 A
0.9 V @ 0.75 A
1.8 V @ 0.15 A
1.0 V/3.3 V @ 1.5 A
1.2 V @ 5 A
2.5 V @ 0.4 A
NXP Technology
Non-NXP Technology
NXP PMIC | Rails used | Key features
FS56 + PF53 + PF8150 | FS56: 2 switchers; PF53: 1 buck (8 A); PF8150: 7 bucks + 4 LDOs | Scalable high-current power platform for Kintex™ UltraScale+ AU20P/25P, enabling ADAS, machine vision and edge AI applications.
Note: The Power Solution is for reference. The user should optimize the power tree based on actual use case with real load current requirement of each power rail.
Optional Technology
Wake up
12 V / 24 V VBAT
PGOOD
Reserved
Reserved
DDR
terminator
LDO3
1.5 V to 5.0 V @ 0.4 A
BUCK3
0.4 V to 1.8 V @ 2.5 A
LDO3
1.5 V to 5.0 V @ 0.4 A
5
1
2
3
4
6