## Slide 1: UJA116x IO board introduction and upgrade to uja116xa v1.2
James LIU, peter buehring ivn s&a 2019-10-21

## Slide 2: Brief Introduction of the UJA116x IO board (old version)
This small board supports the evaluation of the UJA116x HS-CAN mini-SBC. Its size is 36.8 x 25.4 mm2
The IO board is in the sample store so that customers or distributors can apply it.
Designed with Altium Designer v10
6 different boards with 6 part No. (12NC), 5 BOMs / schematics, but share 2 layout (only difference in the silk layer, i.e. different characters)
Part Number | 12NC | Device (SBC) | Schematic | Layout
OM14511/U1161JP | 935337156599 | UJA1161TK | UJA1161_demo_board.SchDoc | UJA1161~3_demo_board.PcbDoc
OM14511/U1162JP | 935337157599 | UJA1162TK | UJA1162_demo_board.SchDoc | 
OM14511/U1163JP | 935337158599 | UJA1163TK | UJA1163_demo_board.SchDoc | 
OM14511/U1164JP | 935337159599 | UJA1164TK | UJA1164_demo_board.SchDoc | UJA1164~8_demo_board.PcbDoc
OM14511/U1168FJP | 935337161599 | UJA1168TK/FD | UJA1167~8_demo_board.SchDoc | 
OM14511/U1168VFJP | 935337162599 | UJA1168TK/VX/FD |  | 

## Slide 3: UJA116x IO board image

## Slide 4: Production Process Nowadays
Sample store initiate the replenish request to NXP AE (James Liu, jian.liu@nxp.com), via email.
PCB supplier (Kingbrother, NXP China qualified supplier) produce the board PCB.
NXP AE send the SBC (UJA116x) and choke (from TDK or Wuerth Elecktronik) to PCB supplier.
PCB supplier purchase the other components, such as resistor, capacitor, diode, connector, and assemble the boards.
Boards ship to NXP AE for test manually.
Boards ship to the sample store.
All the cost covered by NXP Shanghai.

## Slide 5: UJA116x upgrades to UJA116xA
Now new UJA116xA is released, and the UJA116x IO boards will be stopped and upgrades to UJA116xA IO boards (TJA1145A and UJA1166A IO boards will be added in)
There will be new Board IO, new 12NC.
Some of the schematics can be reused, but need modification, see next slides. BOM for each part number will be available.
What else information/documents do Boards Solutions need for future production and sample store replenish ?

## Slide 6: New UJA116xA / TJA1145A IO board
The new UJA116xA IO board family contains 8 different device / part number
Schematics can be reused (Altium Designer v10 format)
New board name | New Device | Old Device | Reusable Schematic | Reusable Layout
UJA1161A-EVB | UJA1161ATK | UJA1161TK | UJA1161_demo_board.SchDoc | UJA1161~3_demo_board.PcbDoc
UJA1162A-EVB | UJA1162ATK | UJA1162TK | UJA1162_demo_board.SchDoc | 
UJA1163A-EVB | UJA1163ATK | UJA1163TK | UJA1163_demo_board.SchDoc | 
UJA1164A-EVB | UJA1164ATK | UJA1164TK | UJA1164_demo_board.SchDoc | UJA1164~8_demo_board.PcbDoc
UJA1168AF-EVB | UJA1168ATK/F | UJA1168TK/FD | UJA1167~8_demo_board.SchDoc | 
UJA1168AXF-EVB | UJA1168ATK/XF | UJA1168TK/VX/FD |  | 
UJA1166A-EVB | UJA1166ATK |  | UJA1162_demo_board.SchDoc | UJA1161~3_demo_board.PcbDoc
TJA1145A-EVB | TJA1145ATK/FD |  | UJA1167~8_demo_board.SchDoc | UJA1164~8_demo_board.PcbDoc

## Slide 7: UJA116xA / TJA1145A IO board schematic requirement

## Slide 8: UJA1168AF-EVB Refer to Old UJA1168 IO board schematic

## Slide 9: UJA1168AXF-EVB Refer to Old UJA1168 IO board schematic
Replace R12 with a capacitor (4.7 µF same footprint, e.g. 0805)

## Slide 10: UJA1166A-EVB Refer to Old UJA1162 IO board schematic
Add a capacitor to GND (10nF) at VIO (pin 5)
Remove R10
Add back the resistor (R11) and LED (D04) at V1 (pin 3, similar as previous UJA1168AXF-EVB)

## Slide 11: UJA1164A-EVB Refer to Old UJA1164 IO board schematic

## Slide 12: UJA1163A-EVB Refer to Old UJA1163 IO board schematic

## Slide 13: UJA1162A-EVB Refer to Old UJA1162 IO board schematic
Add a capacitor to GND (10nF) at VIO (pin 5)
Remove R10

## Slide 14: UJA1161A-EVB Refer to Old UJA1161 IO board schematic
Add a capacitor to GND (10nF) at VIO (pin 5)
Remove R10

## Slide 15: TJA1145A-EVB Refer to Old UJA1168 IO board schematic
Add a capacitor to GND (10nF) at VIO (pin 5)
Remove R10
TJA1145ATK/FD

## Slide 16: UJA116xA / TJA1145A IO board layout requirement

## Slide 17: Arduino connector pin selection, part 1
For those SBCs without SPI, their pins (HVSON14 pin number 6, 8, 11, 14) can be connected to the same position on Arduino J2. The MCU takes care to configure the pinning.
RXD/TXD via solder bridges, DNP by default.
20
19
2
1
1
2
15
16
GND, SCK, SDO, SDI, SCSN
RXD, TXD
VIO, RSTN, VCC, GND, GND
J2 (Arduino)
J3 (Arduino)

## Slide 18: Arduino connector pin selection, part 2
Care need to be taken for HVSON14 pin 3 and 5. They have different functionality for the variants.
1
2
15
16
VIO, RSTN, VCC, GND, GND
J3 (Arduino)
HVSON14 pin No. | Functionality | Variants | Arduino J3 pin No.
Pin 3 | V1 | 1168, 1166, 1164, 1163 | 3, via jumper.
 | BUF | 1162, 1161 | No connection
 | VCC | 1145 | 9, via 0Ω resistor
Pin 5 | RSTN | 1168, 1164, 1163 | 5
 | VIO | 1166, 1162, 1161, 1145 | 3

## Slide 19: Connector for customer usage
Besides the Arduino connector (headers to the bottom), another connector (headers to the top, but don’t place) can point the chip signals outside the board while customers don’t use the Arduino MCU board. Customer can solder the header by themselves.
Put different characters (silk screens) for different variants, and leave empty for “i.c.”
Pin 1, TXD
Pin 4, RXD
Pin 6, SDO / CTS
Pin 11, SDI / i.c.
Pin 8, SCK / i.c.
Pin 14, SCSN / SLPN / STBN
GND
Pin 3, V1 / BUF / VCC
Pin 5, RSTN / VIO
Pin 7, INH / VEXT / i.c.
Pin 9, WAKE / i.c.
GND

## Slide 20: Board overview
BAT
GND
CANH
CANL
Arduino J2
Arduino J3
Customer connector (DNP)
DC plug
UJA/TJA
(HVSON14)